## Wheel Loader 966

Features
1. The wheel loader 966 uses engine from Shanghai Diesel Engine Co., Ltd.
2. The KD switch brings optimal efficiency and easy operation of the wheeled loader.
3. Our construction machinery is installed with dry type axle from MERITOR.
4. Reliable ZF gearbox and torque converter.
5. Bucket automatic leveling is available
6. The boom comes with position limitation function.
7. For high seal performance and optimal reliability, this with Weichai engine wheel loader is engineered with combined seal cylinder.

Technical Specification:

| Overall Dimension |
| --- |
| 1 | Length (with bucket on ground) | 8580(mm) |
| 2 | Width (to the outside of wheels) | 2897(mm) |
| 3 | Bucket width | 3048(mm) |
| 4 | Height (to the top of the cab) | 3532(mm) |
| 5 | Wheel base | 3300(mm) |
| 6 | Tread | 2300(mm) |
| 7 | Min. ground clearance | 403(mm) |
| Main Technical Specifications |
| 1 | Rated loading capacity | 6000(kg) |
| 2 | Operating weight | 19100(kg) |
| 3 | Rated bucket capacity | 3.5(m3) |
| 4 | Max. breakout force | 190KN |
| 5 | Max. driving force | 180KN |
| 6 | Max. dumping clearance | 3393(mm) |
| 7 | Dumping reach | 1365(mm) |
| 8 | Dumping angle at any position | ≥45° |
| 9 | Digging depth (with bucket bottom horizontal) | 212(mm) |
| 10 | Min. turning radius |
|  | (1) Outside of bucket | 6970(mm) |
|  | (2) Outside of front wheel | 6258(mm) |
| 11 | Articulation angle | 38±1° |
| 12 | Oscillating angle of rear axle | ±12° |
| 13 | Lifting time of bucket | 5.8(sec.) |
| 14 | Lowering time of bucket | 3.2(sec.) |
| 15 | Dumping time | 1.5(sec.) |
| 16 | Traveling speed (4 forward and 3 reverse gear) |
|  | (1)1st gear (forward & reverse) | 6.5(km/h) |
|  | (2)2nd gear (forward & reverse) | 11.8(km/h) |
|  | (3)3rd gear (forward & reverse) | 23.5(km/h) |
|  | (4)4th gear (forward) | 37.2(km/h) |
| Diesel Engine for Wheel Loader |
| 1 | Model | Shanghai Diesel Engine SC11CB240.1G2B1 |
| 2 | Type | Direct injection, turbocharged, water cooled |
| 3 | Rated output | 174.5(kW) |
| 4 | Piston diameter/stroke | 121/152(mm) |
| 5 | Total engine displacement | 10.5(L) |
| 6 | Model of starting motor | 4N3181 |
| 7 | Power of starting motor | 7.5(kW) |
| 8 | Voltage of starting motor | 24(V) |
| 9 | Rated speed | 2200(r/min) |
| 10 | Max. torque | 912(N.m)/1400rpm |
| 11 | Starting type | Electrical starting |
| 12 | Min. specific fuel consumption | 238(g/kW.h) |
| 13 | Engine specific oil consumption | 0.95-1.77(g/kW.h) |
| 14 | Net weight | 960(kg) |
| Transmission System for Wheel Loader |
| I. Torque Converter |
| 1 | Type | 3-element, single stage |
| 2 | Torque ratio | 2.55 |
| 3 | Max. dia. of flow path | 340(mm) |
| 4 | Cooling type | Pressure oil circulating |
| II. Gear Box |
| 1 | Model | ZF4WG200 |
| 2 | Type | Power shift, constant-mesh spur gear |
| 3 | Gear shift position | 4 forward and 3 reverse gears |
| III. Axle and Tire |
| 1 | Type of main reducer | Spiral bevel gear, single stage |
| 2 | Gear ratio of main reducer | 4.875 |
| 3 | Type of final reducer | Single stage planetary |
| 4 | Gear ratio of final reducer | 4.94 |
| 5 | Total gear ratio | 24.0825 |
| 6 | Size of tire | 23.5-25-20PR L-3 |
| Working Device Hydraulic System |
| 1 | Model of oil pump | JHP2080-Gj0020-XF (From Jinan Hydraulic Pump Co., Ltd.) |
| 2 | System pressure | 20(MPa) |
| 3 | Model of distribution valve | DXS-00(from Zhejiang Linhai) |
| 4 | Model of pilot valve | D32II |
| 5 | Dimension of lifting cylinder (D×L) | Ф160×90×874(mm) |
| 6 | Dimension of tilting cylinder (D×L) | Ф210×110×575(mm) |
| Steering System for Wheel Loader |
| 1 | Type | Articulated frame, full-hydraulic steering |
| 2 | Model of steering pump | JHP2080S (from Jinan Hydraulic Pump Co., Ltd.) |
| 3 | Steering system pressure | 16MPa |
| 4 | Dimension of steering cylinder | Ф100×50×425(mm) |
| 5 | Model of redirector | BZZ3-100 |
| Braking System |
| 1 | Type of service brake | Caplier disc brake, dual pipelines, air-over-oil activated 4 wheel brake |
| 2 | Air pressure | 7-8(kgf/cm2) |
| 3 | Type of emergency brake | Automatic cutting-off air brake |
| 4 | Type of parking brake | Drum brake, manual control cutting-off air brake |
| Oil Capacity for Wheel Loader |
| 1 | Fuel(diesel) | 350(L) |
| 2 | Engine lubricating oil | 28(L) |
| 3 | Braking system | 2×2(L) |
| 4 | Oil for converter and gear box | 45(L) |
| 5 | Oil for hydraulic system | 250(L) |
| 6 | Oil for driving axles (F/R) | 30(L)+24(L) |