## Motor Grader 722-5

1. The 722-5 motor grader is equipped with original ShangChai diesel engine. 
2. The sing-handle and electro-hydraulic controlled power-shift transmission adopts 6 forward and 3 reverse gear design, making operation easy and convenient.
3. The adopted NO-SPIN differential with auto lock and unlock function provides high stability and powerful traction.
4. This motor grader features ideal axel load allocation, so that it can cut hard surface while maintaining great stability.
5. Due to the efficient hydraulic system, every working part can be fully controlled. 
6. Through the flexible blade suspension system and articulated frame, a variety of tasks can be accomplished. 
7. The vehicle can be used to complete heavy-duty work, due to its box-type frame and advanced transmission system.

Specifications of Motor Grader

| Overall Dimension |
| --- |
| 1 | Length | 9235mm |
| 2 | Width | 4320mm |
| 3 | Height(To the top of the cab) | 3370mm |
| 4 | Wheel base | 6100mm |
| 5 | Tread | 2120(mm) |
| Main Technical Specification |
| 1 | Operating weight | 16600kg |
| 2 | Blade length | 4320mm |
| 3 | Blade height | 545mm |
| 4 | Shovel Blade thickness | 16mm |
| 5 | Max lifting height | 450mm |
| 6 | Max grading depth | 535mm |
| 7 | Min. turning radius | 7400mm |
| 8 | Pivot angle frame | +26° |
| 9 | Max turning angle(front wheel) | +49° |
| 10 | Oscillating angle of front axle | +16° |
| 11 | Min ground clearance | 430mm |
| 12 | Cut angle | 29-77° |
| 13 | Traveling speed(Km/h), 6 forward and 3 reverse |
|  | (1) Ⅰ gear forward | 6.8 |
|  | (2) Ⅱ gear forward | 10.3 |
|  | (3) Ⅲ gear forward | 15.3 |
|  | (4) Ⅳ gear forward | 22.7 |
|  | (5) Ⅴ gear forward | 32 |
|  | (6) Ⅵ gear forward | 47 |
|  | (7) Ⅰ gear reverse | 6.8 |
|  | (8) Ⅱ gear reverse | 15.3 |
|  | (9) Ⅲ gear reverse | 32 |
| Diesel Engine |
| 1 | Model | ShangChai SC11CB220G2B1 engine |
| 2 | Type | Direct injection. Turbocharged. Water cooling |
| 3 | Rated output | 162 kW |
| 4 | Inter-bore of cylinder/Stroke | 121/152 (mm) |
| 5 | Total exhaust of cylinder | 10.49 (L) |
| 6 | Model of starting motor | KB-24V |
| 7 | Power of start motor | 7.5(KW) |
| 8 | Voltage of starting motor | 24(V) |
| 9 | Rated speed | 2200(r/min) |
| 10 | Max. Torque | 844±6%(N.M)/1400(r/min) |
| 11 | Starting type | Electric |
| 12 | Min. specific fuel consumption | <235(g/Kw.h) |
| 13 | Engine specific oil consumption | 0.7(g/Kw.h) |
| 14 | Net weight | 960(kg) |
| Transmission System |
| 1. Torque Converter |
| 1 | Model | 6WG180 (ZF technology) |
| 2 | Type | 3-elements.single stage |
| 3 | Torque ratio | 1.94 |
| 4 | Cooling type | Pressure oil circulating |
| 2. Transmission Case |
| 1 | Model | 6WG180 (ZF technology) |
| 2 | Type | power shift, single-shift lever, netural-shift lock device |
| 3 | Gear shift position | 6 Forward and 3 reverse gears |
| 3. Axle and Tire |
| 1 | Type of main reducer | spiral bevel gear, single stage |
| 2 | Gear ratio of main reducer | 3.583 |
| 3 | Type of final reducer | Single stage chain-drive |
| 4 | Gear of ratio of final reducer | 3.75 |
| 5 | Gear ratio | 13.436 |
| 6 | Max. drawing force | 105KN |
| 7 | Tandem drive | Double row roller-chains |
| 8 | Size of tire | 17.5-25-14PR(standard) 14.00-24-16PR(optional) |
| Working Device Hydraulic System |
| 1 | Model of oil pump(include steering pump) | CBGj2045/1025 |
| 2 | System pressure | 175(kgf/cm2) |
| 3 | Model of distribution valve | HUSCO5000-D HUSCO5000-D |
| 4 | Hydraulic lock | KAYABA technology |
| 5 | Model of oil motor | EATON, JS-130 |
| Steering System |
| 1 | Type | Fore Tire deflexion |
| 2 | Model of steering gear | BZZ1-E160B+ FKA-163022 |
| 3 | System pressure | 16MPa |
| Brake System |
| 1 | Type of traveling brake | Hydraulic assisted and inner-expanding hoof brake |
| 2 | System pressure | 100(kgf/cm2) |
| 3 | Type of parking brake | Mechanical and inner-expanding brake |
| Front Driving System |
| 1 | Type of driving pump | Axial constant displacement piston pump |
| 2 | Model of driving pump | FR-L-074B-LS-25-20-NN(Sauer) |
| 3 | Type of driving motor | Radial variable displacement piston motor |
| 4 | Model of driving motor | 5420100AA(Finland, Black Bruin) |
| Oil Capacity |
| 1 | Fuel(diesel) | 400L |
| 2 | Engine lubricating oil | 24L |
| 3 | Oil for converter and gear box | 28L |
| 4 | Oil for hydraulic system | 116L |
| 5 | Oil for driving rear axles | 18L |
| 6 | Tandem box | 84L |