## ZG3365LC-9C Hydraulic Excavator

Main Features
1. The ZG3365LC-9C excavator employs the original Cummins C series engine imported from the US, which provides outstanding durability and suitability for high strength and heavy load works in harsh conditions, combined with strong power, low oil consumption and compliance with Euro II emission qualification. 
2. Under a negative flow and total power control system with action coordination function, the digging machine has large digging force, high efficiency and perfect flexibility. 
3. Equipped with High strength large structural components, heavy moving arm and bucket rod, reinforced bucket and anti-collision platform, the excavator can be used in severe working conditions such as mine. 
4. It is provided with a lengthened and widened chassis, ensuring high strength, higher safety and stability. 
5. Intelligent electronic monitoring system provides real time monitoring, automatic fault diagnosis and warning, maintenance reminding functions. 
6. The mine excavator comes with a new driver cab that has a fully automatic air conditioning, and offers spacious and comfortable driving feeling. The cab comes in various protections for different working conditions. 
7. Automatic refueling system is optional. One-key operation makes it easy to use.

1. Overall Dimension of ZG3365LC-9C Hydraulic Excavator

2. Working Range of ZG3365LC-9C Hydraulic Excavator

Technical Parameters of Hydraulic Excavator

| Item | Unit |  |
| --- | --- | --- |
| Rated standard bucket capacity (standard SAE) | m3 | 1.50 |
| Operating weight | kg | 34000 |
| Overall power | kW | 198/2000 kW/rpm |
| Dimension | Total length (in transportation condition) A | mm | 11140 |
|  | Total width (in transportation condition) (with 600mm track) B | mm | 3280 |
|  | Total height (in transportation condition) C | mm | 3280 |
|  | Height (from ground to the top of the cab) E | mm | 3235 |
|  | Ground clearance of counterweight F | mm | 1212 |
|  | Min. ground clearance of chassis H | mm | 500 |
|  | Min. rotation radius | mm | 3450 |
|  | Min. rotation radius of the working device | mm | 4310 |
|  | Track wheelbase J | mm | 4050 |
|  | Track gauge M | mm | 2680 |
|  | Standard width of track shoe N | mm | 600 |
| Performance | Working range | Max. digging depth B | mm | 7380 |
|  |  | Max. vertical digging depth C | mm | 6480 |
|  |  | Max. digging radius A | mm | 11110 |
|  |  | Max. digging depth on ground A’ | mm | 10920 |
|  |  | Max. digging height D | mm | 10210 |
|  |  | Max. dumping height E | mm | 7110 |
|  | Max. digging force (ISO standard) | Bucket | kN | 210 |
|  |  | Bucket rod | kN | 161 |
|  | Max. tractive force | kN | 296 |
|  | Rotating speed | rpm | 9.7 |
|  | Travel speed | Max. travel speed | km/hr | 4.8 |
|  |  | Min. travel speed | km/hr | 2.8 |
|  | Gradeability | Degree (%) | 35 (70%) |
|  | Ground pressure | kgf/cm2 | 0.55 |

Components of Hydraulic Excavator

| Diesel engine | Model |  | Cummins 6CTAA8.3-C250 |
| --- | --- | --- | --- |
|  | Type |  | 6-cylinders direct-injection turbocharged engine |
|  | Performance | Rated power | Hp (kW)/rpm | 250 (186)/2200 |
|  |  | Max. torque | N.m/rpm | 1219/1300 |
|  | Starting motor |  | 24V 7.2kW |
|  | Alternator |  | 24V 70A |
|  | Accumulator |  | 2×12V×120A.h |
|  | Radiator |  | Water radiator+ oil cooler+ intercooler radiator +oil cooler+ intercooler |
| Track frame | Track roller |  | 9pcs on each side |
|  | Joe sprocket |  | 2pcs on each side |
|  | Track shoe |  | 48pcs on each side |
| Hydraulic system | Main pump | Model |  | Kawasaki |
|  |  | Type |  | Axial variable piston pump |
|  |  | Displacement | cc/rev | 2×140 |
|  |  | Rated flow | L/min | 2×280 |
|  | Pilot pump | Type |  | Single-stage quantitative gear pump |
|  |  | Displacement | cc/rev | 15 |
|  |  | Rated flow | L/min | 30.0 |
|  | Control valve | Model |  | Kawasaki |
|  |  | Operating mode |  | Hydraulic pilot control |
|  |  | Pressure of main relief valve | Mpa | 34.3 |
|  | Rotary motor | Model |  | Kawasaki |
|  |  | Type |  | Axial quantitative piston motor |
|  |  | Operating pressure | Mpa | 27.5 |
|  |  | Braking system |  | Auto release, hydraulic control, spring action |
|  | Travel motor | Model |  | Kawasaki |
|  |  | Type |  | Axial quantitative piston motor |
|  |  | Operating pressure | Mpa | 34.3 |
|  |  | Braking system |  | Multi-disc wet negative pressure brake |
|  | Hydraulic cylinder |  |  | Boom | Bucket rod | Bucket |
|  |  | Inner diameter of cylinder | mm | 140 | 160 | 140 |
|  |  | Diameter of piston | mm | 100 | 110 | 100 |
|  |  | Stroke | mm | 1480 | 1810 | 1285 |

Oil Capacity of Hydraulic Excavator

| 1 | Fuel tank capacity (diesel) | 600 (L) |
| --- | --- | --- |
| 2 | Hydraulic oil tank capacity | 310 (L) |

Related Names
Heavy Construction Vehicle | Earthmoving Device | Digging Machine | Construction Machinery | Track Excavator